## Slide 1: CatSim 0.1.0 Demo
Madhuri Nagare
My Department
Purdue University
18th Sept. 2020

## Slide 2: What is CatSim
CatSim is “computer assisted tomography simulator”
    Simulates x-ray projections including CT
    Originally developed in MATLAB
XCIST: X-ray-based cancer imaging simulation toolkit
    Open-source python version
    Simulates of the X-ray and CT imaging process, including reconstruction algorithms, phantoms with and without realistic tumors, and a dose estimation tool.
XCIST v 0.1.0 includes generic third-generation CT simulation capability with
    geometric oversampling
    quantum noise
    electronic noise
    beam hardening
    voxelized phantoms
This project is supported by the National Cancer Institute of the National Institutes of Health under Award Number U01CA231860 (ITCR grant)

## Slide 3: Installation
OS requirements: Windows/ Linux
Instructions on the documentation page are relevant to windows and complicated
Installation instructions for Linux system with Anaconda and git installed
Open terminal
>> git clone https://github.com/xcist/CatSim.git
>> conda create -n catsimenv python=3.7
>> conda activate catsimenv
(catsimenv) >> pip install numpy
(catsimenv) >> cd ~/CatSim (catsimenv) >> pip install .
(catsimenv) >> cd examples
(catsimenv) >>python Sim_Sample.py
....
....
Simulation is done
(catsimenv) >> conda deactivate
>>
The documentation mentions
git clone https://github.com/xcist/code.git However, it doesn’t work.
(Required !)
Should generate a line plot if installation was successful

## Slide 4: Defining a Simulation Experiment
Create Sim_example.py
Open terminal
>> conda activate catsimenv
(catsimenv) >>python Sim_example.py
....
Simulation is done
(catsimenv) >> conda deactivate
>>
Recommended file name format: Sim_<name>.py

## Slide 5: Configuration Files
All simulation experiments are defined by five configuration files (located at ~/CatSim/catsim/cfg
File name | Defines | 
Scanner_<name>.cfg | scanner parameters including scanner geometry, x-ray tube, detector | Scanner_Default.cfg
Phantom_<name>.cfg | file that defines the phantom to be ‘scanned’ | Phantom_Default.cfg
Protocol_<name>.cfg | scan protocol, including scan technique, spectrum, filtration, etc. | Protocol_Default.cfg
Physics_<name>.cfg | simulation-level parameters that determine the accuracy at which the simulation is performed | Physics_Default.cfg
Recon_<name>.cfg | reconstruction parameters | Recon_Default.cfg